## Slide 1: ESE-2014 Digital Signal Processing and Storage
Linchen Wang

## Slide 2: Review
Sample
Analog signal
(Continuous in both time and amplitude)
Quantize
Sampled-data signal
(Discrete in time and continuous in amplitude)
Encode
Discrete time discrete amplitude signal
Digital signal

## Slide 3: Outline
Types of signal
Some types of sequences in discrete-time signal
Operation on sequences

## Slide 4: Types of signal: Discrete time signal
Discrete time signal: It is a time series consisting of a sequence of quantities.
It may been obtained by sampling from a continuous-time signal.

## Slide 5: Types of signal: Periodic signal
Periodic signal: A signal if it completes a pattern within a measurable time frame, call a period and repeats that pattern over identical subsequent periods.
Period: it is the smallest value of T satisfying for all .

## Slide 6: Types of signal: Energy signal & Power signal
Energy signal and Power signal
The terms signal energy and signal power are used to characterize a signal.

## Slide 7: Types of signal: Energy signal & Power signal
Continuous-time signal
Discrete-time signal
If , the signal is an energy signal.
If , the signal is a power signal.

## Slide 8: Types of signal: Energy signal & Power signal
A signal can be an energy signal, a power signal, or neither.
A signal can not be both an energy signal and a power signal.
Note, the power for an energy signal is zero (P=0).
The energy for a power signal is infinite (E=).

## Slide 9: Types of signal: Even & odd signal
One of characteristics of signal is symmetry that may be useful for signal analysis.
Even signals are symmetric around vertical axis.
Odd signals are symmetric about origin.
An odd signal must be 0 at , means odd signals pass the origin.

## Slide 10: Some types of sequences in discrete-time signal
X(n) = {…, x(-1), x(0), x(1), …}
Up-arrow indicates the sample at n = 0.
E.g. x(n) = {2, 1, -1, 0, 1, 4, 3, 7}
x = [2, 1, -1, 0, 1, 4, 3, 7]
n = [-3,-2,-1,0, 1, 2, 3, 4]

## Slide 11: Unit sample sequence

## Slide 12: Unit sample sequence
Instead of use zeros(1, n)
Function [x, n] = impseq (n0, n1, n2)
% Generates x(n) = delta(n-n0); n1 <= n <= n2
% [x, n] = impseq (n0, n1, n2)
n = [n1: n2]; x=[(n-n0)==0];

## Slide 13: Unit step sequence
u
u

## Slide 14: Unit step sequence
Instead of use ones(1, n)
Function [x, n] = stepseq (n0, n1, n2)
% Generates x(n) = u(n – n0); n1 <= n <= n2
% [x, n] = stepseq (n0, n1, n2)
n = [n1 : n2]; x = [(n – n0) >= 0];

## Slide 15: Some types of sequences in discrete-time signal
Real-valued exponential sequence
n = [0: 10]; x = (0.9).^n;
Complex-valued exponential sequence
E.g. 10
n = [0: 10]; x = exp((2+3j)*n);

## Slide 16: Some types of sequences in discrete-time signal
Sinusoidal sequence
E.g.
n=[0: 10]; x = 3*cos(0.1*pi*n+pi/3) + 2*sin(0.5*pi*n);

## Slide 17: Some types of sequences in discrete-time signal
Random sequence
rand(1,N): generates a length n random sequence whose elements are uniformly distributed between [0, 1].
randn(1,N): generates a length n Gaussian random sequence with mean 0, and variance 1.
Randi(N): generates a length n uniform distribution between [1,N].

## Slide 18: Some types of sequences in discrete-time signal
Periodic sequence
, N is the fundamental period.
We x tilde to denote a periodic sequence
x = [x1, x2, x3, … , xn] % fundamental period
xtilde = x’*ones(1,p) % p columns of x; x is a row vector period;
xtilde = xtilde(:); % long column vector
xtilde = xtilde’; %long row vector

## Slide 19: Operation on sequences
There are some basic sequence operations, and let us to talk about their Octave (Matlab) equivalents.
1. Signal addition: This is a sample-by-sample addition given by
It is implemented in MATLAB by the arithmetic operator “+”. However, the lengths of x1(n) and x2(n)must be the same.

## Slide 20: Operation on sequences
If sequences are of unequal lengths, or if the sample positions are diﬀerent for equal length sequences, then we cannot directly use the operator “+”. We have to first augment x1(n) and x2(n) so that they have the same position vector n, which means they should have same length.

## Slide 21: Operation on sequences
function [y,n] = sigadd(x1,n1,x2,n2)
% implements y(n) = x1(n)+x2(n)
% [y,n] = sigadd(x1,n1,x2,n2)
% y=sum sequence over n, which includes n1 and n2
% x1=first sequence over n1
% x2=second sequence over n2 (n2 can be different from n1)
% n=min(min(n1),min(n2)):max(max(n1),max(n2)); % duration of y(n)
y1 = zeros(1,length(n)); y2 = y1; % initialization
y1(find((n>=min(n1))&(n<=max(n1))==1))=x1; % x1 with duration of y
y2(find((n>=min(n2))&(n<=max(n2))==1))=x2; % x2 with duration of y
y=y1+y2; % sequence addition

## Slide 22: Operation on sequences
2. Signal multiplication: This is a sample-by-sample (or “dot”) multiplication) given by
It is implemented in MATLAB by the array operator .*.

## Slide 23: Operation on sequences
function [y,n] = sigmult(x1,n1,x2,n2)
% implements y(n) = x1(n)*x2(n)
% [y,n] = sigmult(x1,n1,x2,n2)
% y=product sequence over n, which includes n1 and n2
% x1=first sequence over n1
% x2=second sequence over n2 (n2 can be different from n1)=min(min(n1),min(n2)):max(max(n1),max(n2));
% duration of y(n)
y1 = zeros(1,length(n)); y2 = y1;
y1(find((n>=min(n1))&(n<=max(n1))==1))=x1; % x1 with duration of y
y2(find((n>=min(n2))&(n<=max(n2))==1))=x2; % x2 with duration of y
y=y1 .* y2; % sequence multiplication

## Slide 24: Operation on sequences
3. Scaling: In this operation each sample is multiplied by a scalar α.
An arithmetic operator (*) is used to implement the scaling operation in Octave (MATLAB).

## Slide 25: Operation on sequences
4. Shifting: In this operation, each sample of x(n) is shifted by an amount k to obtain a shifted sequence y(n).
function [y,n] = sigshift(x,m,k)
% implements y(n) = x(n-k)
% [y,n] = sigshift(x,m,k)
n=m+k; y = x;

## Slide 26: Operation on sequences
5. Folding: In this operation each sample of x(n) is flipped around n = 0 to obtain a folded sequence y(n).
function [y,n] = sigfold(x,n)
% implements y(n) = x(-n)
% [y,n] = sigfold(x,n)
y=fliplr(x); n = -fliplr(n);

## Slide 27: Operation on sequences
6. Sample summation: This operation differs from signal addition operation. It adds all sample values of x(n) between n1 and n2.
It is implemented by the sum(x(n1:n2)) function

## Slide 28: Operation on sequences
7. Sample products: This operation also differs from signal multiplication operation. It multiplies all sample values of x(n) between n1 and n2. It is implemented by the prod(x(n1:n2)) function.

## Slide 29: Operation on sequences
E.g. Let x(n) = {1,2, 3, 4, 5, 6, 7, 6, 5, 4, 3, 2, 1}.
↑
Determine and plot the following sequences.
x1(n) = 2x(n - 5) - 3x(n + 4)
Since the sequence is nonzero over
>> n = -2:10; x = [1:7,6:-1:1];
[x1,n1] = sigshift(x,n,5); [x2,n2] = sigshift(x,n,-4);
[x3,n3] = sigadd(2*x1,n1,-3*x2,n2);
subplot(2,1,1); stem(n3,x3);
xlabel(’n’); ylabel(’x3(n)’);

## Slide 30: Operation on sequences
b. x2(n) = x(3 - n) + x(n) x(n - 2)
The first term can be written as x(-(n - 3)). >> [x4,n4] = sigfold(x,n); [x4,n4] = sigshift(x4,n4,3);
[x5,n5] = sigshift(x,n,2); [x5,n5] = sigmult(x,n,x5,n5);
[x6,n6] = sigadd(x4,n4,x5,n5);
subplot(2,1,2); stem(n6,x6);
xlabel(’n’); ylabel(’x6(n)’);